## Slide 1: 5G Overview and Testing Requirements
Jeremy Davis – Solutions Engineer
May 23rd, 2019
.
Notes: Last updated by Corporate Marketing on September 1, 2016.

## Slide 2: Agenda
5G Overview
Network Topology
Network Testing
Questions
Notes: This APJ Partner training is all about hands-on and competitive
  We have heard your voice
  Partners need to gain more confidence in hands-on competitive scenarios rather than just reading paper analyses
  We had consolidated your input, and worked hard to bring in competitor units that you frequently compete against
  Please give 100% effort to maximize this opportunity to learn
Ask partners to look out for untapped adjacent markets (be it lower dynamic range/ lower price/ special feature request/ etc that we do not offer today)
Provide qualitative and quantitative input to VIAVI when raising requests <- I’m not getting a lot of feedback from the OTDR survey distributed earlier.
We have added Field calibration services for a more comprehensive solution, this will give us additional flexibility and reach to offer bundles and upsell and re-farm old installed base <- JX will cover more details in the Executive Track

## Slide 3: 5G Overview

## Slide 4: Introduction to 5G Radio Access
5G technology is based on orthogonal frequency division multiple access (OFDMA) transmission technology, similar to LTE, supporting data modulation from QPSK to 256QAM; however, it incorporates additional flexibility, for example:
Frequency operating bands: :
  Frequency Region 1 (FR1) for sub-6GHz
  Frequency Region 2 (FR2) for millimeter wave (mmWave) between 24GHz and 52GHz
Channel bandwidth: flexibility for wider channel bandwidth configurations;
  FR1 range is from 5MHz to 100MHz
  FR2 is from 50MHz to 400MHz
Carrier aggregation: capability to aggregate two or more component carriers to increase channel bandwidth
Beam forming: ability to generate and shape multiple beams based on phase and amplitude to direct radiated power to the user’s serving area

## Slide 5: 5G RAN Revolution Massive MIMO and Beamforming
M-MIMO and Beamforming Benefits
Massive MIMO is well suited for higher frequency bands (mmWave), allowing a high array of antennas into a small panel or area.
Beamforming improves signal to noise ratio (SINR) concentrating the energy through narrower beams, as well as creating constructive interference (diversity) overlapping multiple beams to improve propagation.
LTE-A
Massive MIMO
20cm
20cm
Beamforming
100 m

## Slide 6: 5G Radio Access Communication Modes
Frequency Band | Tx/Rx Mode
FR1 < 3GHz | FDD, TDD, SDL, SUL
FR1 > 3GHz | TDD
FR2 | TDD
DL
UL
Freq
Time
Power
751 MHz
782 MHz
Freq
Time
Power
DL
DL
UL
3560 MHz
DL
UL
Freq
Time
Power
751 MHz
782 MHz
739 MHz
FDD: Frequency Division Duplex
SDL: Supplemental Downlink
TDD: Time Division Duplex

## Slide 7: 5G RADIO ACCESS TECHNOLOGY ELEMENTS
Source: Nokia

## Slide 8: 5G Network Topology

## Slide 9: 5G brings deeper fiber in fronthaul
Operators are now recognizing that fiber is imperative for a successful 5G rollout.
Symmetric speeds of 1 to 10Gbps and latency of 1 millisecond are required
Average Fiber Count (AFC) in the cable must be increased
5G will require a 20-30 times increase in the number of small cells, Exponential impact on fiber end points.
5G could use PON feeds but design considerations needs to be made on bandwidth availability.

## Slide 10: Fiber Densification Changes the Game
Upgrade from 3G to 4G/5G with fiber densification, more frequent BBUs and Antennas
Ideal: Reuse old fiber if performance is acceptable but some will have to be replaced or added
More points of failure with higher split ratio from RU to BBU and more fiber legs to maintain
Reduced optical loss budgets compared to 3G and 10G is more susceptible to reflectance that distorts the signal
Antenna locations are more vulnerable to roadside accidents
More distribution, path issues.

## Slide 11: Backhaul, Fronthaul, and CRAN
SMALL CELLS
Cell Site
Core Site
BSC/RNC SGW/MME
Mobile Switching Center
Backhaul
Mobile Switching Center
BSC/RNC SGW/MME
Backhaul
RRU
(Radio Radio Unit)
BBU
(Baseband Unit)
FTTA (Fiber to the Antenna)
MACROCELL
Fiber
COAX
RF
Mobile Switching Center
BSC/RNC SGW/MME
Centralized/ Cloud
RAN
Backhaul
Central Site
RRU
Base Station Hotel
Fronthaul

## Slide 12
RU
Midhaul
CU
Today:
Tomorrow:
DU
xHAUL Evolution: Migration for BOTH 4G and 5G
Fronthaull
Backhaul
F1
eCPRI
eS1/Ethernet
RRC
High RLC
PDCP
Low RLC
High MAC
Low MAC
High PHY
Low PHY
RF

## Slide 13: Look Similar?
vCMTS
OTU 8000
Headend
100/10G
Transport optical link
Hub
Node
10GE DWDM
optical link
Test Port
T-BERD/MTS
T-BERD/MTS
Fiber Centralized Test Head
DWDM route validation
Fiber link commissioning at the Hub or at the node
Measures the fiber performance and the quality of any fiber optic interconnections to support migration to 10GE or 100GE transmission
T-BERD/MTS

## Slide 15: Network Testing

## Slide 16: Testing Challenges
Fiber Condition and Continuity
New WDMs added to network
Simply more fiber deployed
Traditional test equipment cannot test through WDMs
Dispersion
Dispersion parameters matter for 10GE transmission
Must select best existing fiber route
Cover the baseline to ensure fiber can support new signals – must characterize
High Fiber Count Cables
More time required to certify
Optimized and efficient test tools and procedures
Single contaminant can create greater impact

## Slide 17: Test Workflow
Best practice, ensure connectors are ALL clean
Certify fiber deployment (splicing, loss, continuity…)
Validate fiber can support 10GE signals.
Required for DWDM continuity and loss budget
Connector Inspection
Fiber Commissioning
Dispersion Testing
DWDM
Charac.
DWDM
Routing
Confirm End-to-End continuity and channel drop
Outside Plant Fiber Characterization
Know the baseline performance of your network.
DWDM-Ready Validation
Qualify DWDM routes with DWDM components (MUX, DEMUX…)

## Slide 18: Fiber Inspection
FiberChek Probe, Sidewinder or P5000i
“Inspect Before you Connect”
  Reduce Network Downtime
  Reduce Troubleshooting
  Optimize Signal Performance
  Prevent Network Damage
Auto-Centering/Auto Focus
Test Objectively and Consistently to IEC Standards – No Subjectivity
Automated Pass/Fail Results
StrataSync results/data management

## Slide 19: MPO Inspection and Certification
Verify Cleanliness of all Bulkhead and Patch Cord Connections
ORL/IL on all Fiber Paths
Identify Link Polarity – Detect cross-over issues – All Links, Adaptors, Patch Cords
Length Measurement enables application testing (40G-SR4 vs 100G-SR4)

## Slide 20: Fiber Characterization
vCMTS
OTU 8000
Headend
100/10G
Transport optical link
Hub
Node
10GE DWDM
optical link
Test Port
T-BERD/MTS
T-BERD/MTS
Fiber Centralized Test Head
DWDM route validation
Fiber link commissioning at the Hub or at the node
Measures the fiber performance and the quality of any fiber optic interconnections to support migration to 10GE or 100GE transmission
T-BERD/MTS

## Slide 21: Fiber Characterization Qualifying fiber for high speed transmission
A comprehensive suite of point-to-point physical layer tests
  Performed during the fiber installation, final commissioning as well as upgrades
  Maximization of existing fiber plant – Mesh network, different fiber types
  Loss budgets are tighter – need precise loss measurement – Bi-directional testing
Test Parameters | Measurement
Connector Inspection | Inspection Scope
Bi-directional Insertion Loss measurement | Loss Test Set
Bi-directional Optical Return Loss (ORL) measurements | Loss Test Set
Bi-Directional connectors/splice measurements | OTDR
Distance Measurement | OTDR
Reflectance measurements | OTDR
Polarization Mode Dispersion (PMD) measurements | PMD analyzer
Chromatic Dispersion (CD) measurement | CD analyzer
Attenuation Profile (AP) measurements | Spectral Analyzer
RU
CU

## Slide 22: CD/PMD Overview
Polarization Mode Dispersion (PMD)
Different polarization modes travel at different velocities causing a Differential Group Delay (DGD) resulting in pulse broadening
PMD varies with time, T°, movement
Chromatic Dispersion (CD)
Different wavelengths (colors) travel at different speeds down the fiber causing the pulses to spread
1x measurement (doesn’t change)
Both CD & PMD can become an issue as you move to Higher Data Rates (10G+)
Notes: One last fiber testing area I wanted to briefly mention is Dispersion Testing.
This testing comes into play when you start putting 10G or higher data rates on the fiber (typical for DAA deployments such as R-PHY).
Dispersion causes the pulses (the “Ones”) to spread out as they travel down the fiber- and with 10G and higher traffic since those pulses are so tightly spaced it can actually result in the pulses overlapping and cause errors or failures.
There are 2 types of Dispersion that need to be tested- Chromatic Dispersion (CD) and Polarization Mode Disperion (PMD).
For CD think of the wavelengths as different colors of light and those colors travel down the fiber at different speeds and cause the pulse to spread out as it travels down the fiber.
For PMD think of the pulse as 3 dimensional. The horizontal axis of the pulse will travel down the fiber at a different rate than the vertical axis which causes the pulse to spread out as it travels down the fiber.
Of course theres test equipment made that can test for both of these dispersions. This becomes more critical as you move into DAA deployments such as Remote PHY.

## Slide 23: Dispersion Parameters
Transmission Type | Transport Speed | PMD Max | CD Max
SONET | OC-192/STM-64 | 10 picoseconds | 1176 ps/nm
Ethernet | 10 Gb/s | 5 picoseconds | 738 ps/nm
SONET | OC-768/STM-256 | 2.5 picoseconds | 64 ps/nm
Ethernet Coherent detection | 100Gb/s | 25 picoseconds | 30000 ps/nm
Ethernet Non coherent detection | 100Gb/s (4x25 Gb/s) | 1.0 picoseconds | 500 ps/nm
Transmission limits determined by the network equipment manufacturers and related to the type of transmission, speed and coding format being implemented.
Main dispersion thresholds according to the transmission rate

## Slide 24: DWDM Link Qualification
xWDM
xWDM
DWDM route validation
Component and
End-to-end loss
Continuity check
Power level

## Slide 25: Optics Testing
Tune optic by wavelength, frequency, or channel number
Run BER test with optic in self loop
PDF report includes optics serial number and tuning information

## Slide 26: Network Connectivity and Throughput Testing
Test Connectivity from RPD location to CCAP location through active and passive components
Measure 10G throughput
Showing simplified QuickCheck, RFC 2544 or Y.1564 could also be used

## Slide 27: Y.1564 SAMComplete
Newer industry standard for single and multiple service Ethernet and IP service activation test
Measure Key Performance Indicators and Bandwidth Profile
  CIR, EIR (Throughput)
  Frame Delay – FD (Latency)
  Frame Delay Variation – FDV (Jitter)
  Frame Loss Rate - FLR
  Committed Burst Size – CBS
  Policing
Fully automated with report generation

## Slide 28: PTP use in Remote PHY (or 5G)
PTP Master
Network
RPD 1
RPD 2
vCMTS
1. PTP Master - source of truth for timing
Subscriber 1
Subscriber 2
3. Each RPD communicates timing information to modems via DTP
2. vCMTS and all RPD devices receive their timing information from PTP master
4. Modems use timing information for upstream communications – 1 ms alignment required by spec

## Slide 29: RF Testing

## Slide 30: RF Testing
Interference Analysis (Real-Time Persistence Spectrum)
  Real time spectrum analysis with persistence display
  RFoFiber : Spectrum and Spectrogram
  RFoAir : Spectrum and Spectrogram (FR1 or sub 6GHz and FR2 from 24GHz to 40GHz)
Signal Analysis (iBW 100MHz)
  4G (LTE, LTE-Advance-Pro, NB-IoT, LTE-M), conformance verification, signal modulation quality.
  5G carrier aggregation, signal modulation quality, beamforming assessment, and coverage profile

## Slide 31: CellAdvisor 5G RF Characterization and Conformance Test
5G RF Characterization
Channel Power, Occupied Bandwidth, ACLR
Adjacent Channel Leakage Ratio
Spurious Emission Mask

## Slide 32: CellAdvisor 5G Persistence Spectrum and Spectrogram
Persistence Real Time Spectrum
Spectrum Analysis, Spectrogram, 3D Spectrogram
Persistence Real Time Spectrogram
Spectrum Analysis, Spectrogram, 3D Spectrogram

## Slide 33: CellAdvisor 5G Channel Scanner and RSSI Power
Channel Scanner
Customizable for Multi-Frequency Band, Multi-Carrier Bandwidth
Multi-Frequency RSSI
Spectrum and RSSI Power Trend

## Slide 34: CellAdvisor 5G Interference Analysis: Triangulation and Radar Chart
Interference Finding
Location: Triangulation
Interference Finding
Location: Radar Chart

## Slide 35: CellAdvisor 5G 5G Carrier Aggregation (x8)
Carrier Aggregation
Multi-Carrier Power Balance
  Spectral impairments in mmWave
  Aggregated 100MHz carriers (x8)
  Carrier’s in-band, contiguous and non-contiguous
  Radio’s power performance of all carrier’s
FREQUENCY
PWR
5G Carrier Scanner (8 component carriers)
Physical Cell ID, Beam ID, Carrier’s Frequency and Power, Beam Power and Quality

## Slide 36: CellAdvisor 5G 5G Beam Analysis
Beamforming Performance
  Increase cell capacity (bandwidth)
  Increase cell coverage (diversity)
Beam 1
Beam 2
Beam n-1
Beam n
5G Beam Analyzer (8 strongest beams)
Physical Cell ID, Beam Index, Beam Power, P-Sync Power, Beam SNR

## Slide 37: CellAdvisor 5G 5G Route Map Coverage
5G Coverage Mapping
  Cell Coverage
  Beam Availability
  Beam Propagation
5G Route Map (Coverage)
Physical Cell ID, Beam Index, Beam Power, Beam SNR

## Slide 38: Questions?