## Slide 1
Safety
When
Working Aloft

## Slide 2: Working Aloft
Where does safety start?
  Senior leadership
    Has to set the tone for a safe work environment
  Mid-level managers
    Need to enforce the correct attitude
  Everyone
    Needs to think safety first
    Needs to work safely
    Needs to make sure others around you are working safe
    If you see someone not working safely, say something!

## Slide 3: Personal Protective Equipment
ANSI Z89.1 approved hardhat must be worn
All field employees are required to wear steel shank boots
ANSI Z87 approved safety glasses are required
Class 2 high visibility safety apparel must be worn while working within the “right of way”
Class 3 must be worn during nighttime operations

## Slide 4: Electrical Safety
No employee shall approach or take any conductive object closer to any electrically energized overhead power lines than:
  300 V or less…………………………………..…………Avoid Contact
  Over 300 V, not over 750 V……………………..12 inches
  Over 750 V, not over 2 kV………………………..18 inches
  Over 2kV, not over 15 kV…………………………24 inches
  Over 15kV, not over 37kV………………………..36 inches
  Over 37 kV, not over 87.5 kV……………..……42 inches
  Over 87.5 kV, not over 121 kV…………………48 inches
  Over 121 kV, not over 140 kV………………….54 inches

## Slide 5: Electrical Safety
AC Voltage Probe
The AC Voltage Probe is a hand-held device for detecting the presence or absence of 50-1000 volts AC.
No contact is required for operation and current flow is not necessary to locate voltage.
If AC voltage is present, the tip will glow red and you will hear an audible tone.

## Slide 6: Utility Poles
Look for tags or a painted X on the pole which identify the pole as unsafe.
    Do not use a ladder on these poles!
Become familiar with the marking system used by the utility companies in your service area.
“DO NOT CLIMB” Tags:

## Slide 7: Utility Poles
Would you take the time to test this pole?
  Inspected in 2018
  Pole looks in good shape, right?
  Lets look at another picture of the same pole
When should you test a pole?

## Slide 8: Utility Poles
Yes, same pole, same day!
This happened in 2019
  Probably within months of being tagged!
  A Tech was injured in the fall
  How could this accident been avoided?
    Better inspection techniques?
    Pole testing by Tech?
When should you test a pole?

## Slide 9: Utility Poles
After a visual inspection, one or more of the following tests should be
  Prod Test
  Hammer Test
  Rocking Test
Structural damage is often hidden from view.
These tests will expose hidden problems
Pole Tests

## Slide 10: Utility Poles
The prod test is used to check the base of the pole for rot.
    Jab a screwdriver into the pole about 2" below ground level.
    If it penetrates easily, clear away the dirt for further inspection.
    Test the circumference at approximately 2" intervals.
Prod Test

## Slide 11: Utility Poles
Starting near ground level, strike repeatedly around the circumference of the pole.
    A solid sound indicates good wood.
    A hollow sound indicates core rot
    slapstick sound indicates shell rot.
Hammer Test
What do you see wrong in this picture?

## Slide 12: Utility Poles
Apply a horizontal force to the pole
  rock it back and forth in a direction perpendicular to the line.
  Exercise caution to avoid causing power lines to swing together.
Apply the force to the pole
  Push it with a pike pole, ladder, or pulling the pole with a rope.
  If you hear the pole cracking during the test, it is unsafe.
Rocking Test

## Slide 13: Utility Poles
Elevator shafts
  If a stepped pole has elevator shafts, the steps may be loose and not be able to support a climbers weight.
  Climb stepped poles with caution. Use a climbing strap well climbing stepped poles to maintain fall protection
Elevator Shafts & Stepped Poles

## Slide 14: General Ladder Usage
  A positioning belt and lanyard must always be used.
  At the pole
    Lanyard should be passed through the ladder and around the pole and attached to the D-rings on the positioning belt.
    Whenever possible, the lanyard should be passed around the pole over top of the strand.
  On a Mid-span
    The lanyard should be wrapped around the strand and ladder before attaching to the D-rings on the positioning belt.
Belting on

## Slide 15: General Ladder Usage
Handling
  A solid, confident ladder carry is essential.
  insure that accidents are avoided.
Avoid tree branches and other aerial obstructions.
    Always inspect your walking route before taking the ladder off of your truck.
    Use caution when moving ladders in high traffic areas.
Extension and Straight Ladders

## Slide 16: General Ladder Usage
Ladders should be setup at approximately a 4 to 1 ratio. That is for every 4 feet high the ladder extends, it should be 1 foot out at the base.
When a ladder is placed on the strand, the strand hooks must be “engaged” with the strand.
Avoid placing the ladder on or straddling a tap.
Extend the ladder at least three rungs (2 foot minimum) above any roof
Before placing a ladder against a wall, be sure to retract strand hooks.
Ladders should be tied off or secured in high wind situations.
Extension and Straight Ladders

## Slide 17: Pole Climbing Basic Safety
Always inspect your equipment before each use
Use pole cinch lanyard and a secondary for 100% fall protection
Keep the gaffs sharp and shaped correctly
Use gaff guards when climbers are not being used

## Slide 18: Pole Climbing
Body Belt
Pair of Climbers
Patriot Fall Restricting Device
Secondary Safety Lanyard
Basic Equipment

## Slide 19: Pole Climbing Obstacles:
Avoid signs and other things which may be attached to the pole.
Anything that reduces the ability to either grip the pole with the hands or provide adequate space for the feet should be avoided.

## Slide 20: Aerial Lift Truck Safety

## Slide 21: Aerial Lift Truck Safety
Inspection Report needs to be carried in vehicle while in use
If anything is found deficient, the truck needs to be removed from service until repaired
Lift and truck need to be inspected daily before use
Example of a visual inspection
  Chassis
  Lift
  Other items
Inspection

## Slide 22: Aerial Lift Truck Safety
https://www.wpxi.com/news/top-stories/1-person-taken-hospital-after-pole-falls-onto-bucket-truck/VVVMU4WRKJBHXCLOCK673DIZSM/

## Slide 23: Suspension Trauma
When hanging in a fall harness, the leg straps support the body’s weight.
During this time, the leg straps of the harness crush the femoral arteries on the inside of the legs, cutting off blood circulation.
When the leg muscles are relaxed, veins in the legs can expand dramatically.
The leg muscles are not being used to stand up, they are not contracting, so veins expand.
This allows blood to gather in the legs rather than returning to the heart and lungs for recirculation.
This can result in a 20 percent loss in blood circulation.
What is it?

## Slide 24: Suspension Trauma
The loss of circulation causes the heart to work harder to keep the brain and vital organs supplied with blood.
This results in nausea, unconsciousness, and a drop in blood pressure and heart rate.
This is the onset of circulatory shock.
Circulatory Shock

## Slide 25: Suspension Trauma
Without circulation in the legs, lactic acid builds up
This is then released when the worker is brought down and circulation restored.
High levels can overwhelm the kidneys, liver, and even result in heart failure.
In a technical bulletin, OSHA identified that suspension trauma could be fatal within 30 minutes of the initial fall.
29 CFR 1926.502 (d) (Fall Protection Systems Criteria and Practices).
OSHA requires "prompt rescue of employees in the event of a fall or shall assure that employees are able to rescue themselves."
Dangers

## Slide 26: Suspension Trauma
In standard first-aid training you lie someone down when they have fainted and raise their legs. This will cause all the acidic blood rush back into the body at one time.
If a suspension trauma victim is lain down, even for a short time, they can die of a heart attack or suffer multiple organ failure.
Anyone helping during rescue must stop medical staff from doing this at all costs and explain why.
Rescue

## Slide 27: Suspension Trauma
Lower victim into a sitting position for a minimum of 30 minutes
  so acidic blood is released gradually.
Anyone suspended for more than 10 or 15 minutes will have dangerously high levels of acidic blood in their legs.
If their heart survives the rescue, other organs can be damaged.
Anyone who has suffered from suspension trauma must be sent to hospital for a check-up.
Proper Treatment

## Slide 28: Review
Safety starts at the top, but everyone is responsible for working safe!
Use the education, tools, and protective equipment provided
be aware of your surroundings and the conditions you are working in
Always base decisions on safety