## Slide 1
FTTx Technologies
Paul Runcy, Senior Director, Sales
ADTRAN

## Slide 2: Agenda
Level Set – Today’s HFC Plant
PON – Passive Optical Networks
PON Architectures
RFoG – Radio Frequency over Glass
EPON – Ethernet Passive Optical Networks
DPoE – DOCSIS Provisioning of EPON
GPON – Gigabit Passive Optical Networking

## Slide 3
Level set: The existing HFC Plant

## Slide 4
The primary facility of any cable network
Fiber optic receiver that converts light from the optical distribution system into RF signals
Boosts the RF signal level along the main coaxial cables
Passive device located on the feeder line to provide connection to customer’s drop
Transport RF CATV signals from the tap to the in-house wiring
Electronics used to provide video, audio, telephony, etc. for the customer
Components of the HFC Cable System
Headend
Node
Amplifier
Tap
Drop cable
Customer Premises Equipment (CPE)
Notes: 4

## Slide 5: Traditional Network
Headend / Hub
Outside Plant
Customer Premises
Power
Power
Trunk
Distribution / Feeders
Drops
In a traditional cable network the headend collects all signals and delivers services through a trunk cable.
The trunk cable has numerous amplifiers and accompanying power supplies in order to provide service to each distribution, or feeder cable, connected to it.
The distribution cables and line extenders amplify the signal down towards the taps which connect cable drops to the customer premise.
DOCSIS CMTS
VIDEO
Coax
Transmitter
Receiver
Power
Power
Notes: Highlight:
1 RPR vs. many
1 fiber vs. many
same headend equipment
same practices

## Slide 6: Hybrid Fiber-Coax (HFC) Network
Headend / Hub
Outside Plant
Customer Premises
In an HFC cable network the trunk cable and amplifiers are replaced with fiber optic cables.
At the headend traditional cable services are converted from RF to optical wavelengths, amplified, and sent out a trunk fiber.
Using an optical fiber on the trunk eliminates amplifiers and accompanying power supplies increasing signal quality and network reliability.
Fiber Nodes are used to terminate the trunk fiber and provide RF services to coaxial distribution lines.
Line extenders, RF taps and coax drop cables are used to connect subscribers to the network.
Trunk
Distribution /
Feeder
Drops
DOCSIS CMTS
VIDEO
Fiber
Coax
Node
Transmitter
Receiver
Notes: Highlight:
1 RPR vs. many
1 fiber vs. many
same headend equipment
same practices

## Slide 7
Passive optical networks

## Slide 8: Fiber distribution methods
Port 1
Port 2
Port 3
Point-to-Point
Port 1
*Point-to-Multi-Point
Usually used with xWDM technology to transport Active Ethernet.
Typically referred to as PON and used with EPON, GPON, & RFoG.
Notes: Architectures that allow fiber to be installed up to the premise can generally be separated into two different delivery methods:
Point to point - In a point-to-point architecture each subscriber has a dedicated path from the source of the transmission to the customer location. Active Ethernet is an example of a point-to-point technology.
Point-to-Multipoint – In a point-to-multipoint architecture subscribers are connected to a common physical plant through the use of taps or splitters. Passive Optical Networking (PON) is an example of a point-to-multipoint technology.

## Slide 9: What is a PON?
Passive – no electronics in OSP
Less maintenance, higher reliability
Splitters to allow sharing of network – unpowered, unmanaged
Optical – all fiber
Extremely high bandwidth
Network
Access network technology
Carries voice, video, and lots of data
Point to multipoint
Notes: A PON is a passive optical network. There are no optical repeaters or other active devices in a PON, hence the name "passive." PONs are designed for local loop transmission rather than long distance and serve to bring fiber closer to the customer in order to obtain higher speed.
Since PONs are passive, they require less maintenance and provide higher reliability. Splitters are used to share network resources and are unpowered and unmanaged. Fiber provides extremely high bandwidth capabilities to carry voice, video, and data.

## Slide 10: Migration from Active to Passive
Active components guide traffic
Network devices require power to transmit data
Processors, memory chips, repeaters, and relays
Traditional - Copper
Passive components guide network traffic based on splitting optical wavelengths
Splitters and coupler devices work by passing or restricting light
PON Networks - Fiber
Notes: Traditional networks use active components to guide traffic. Devices such as processors, repeaters, and relays all require power to transmit data.
In contrast, passive optical networks use passive components that guide traffic based on splitting optical wavelengths to end points along the way. These passive components, such as splitters and coupler devices, work by passing or restricting light and do not require power to transmit data. Therefore, PONs use less power and cost less to operate.

## Slide 11: Passive Optical Network (PON)
Headend / Hub
Outside Plant
Customer Premises
A Passive Optical Network extends the fiber optic cabling all the way to the subscriber premise.
This architecture removes all active amplifiers and power inserters from the cable network.
Optical Network Units (ONUs) are used at the customer premise to convert optical signaling into traditional Ethernet, voice, and video services.
Drops
Trunk
Optical Network Units
“ONUs”
Optical Line Terminal
“OLT”
Fiber
Notes: Highlight:
1 RPR vs. many
1 fiber vs. many
same headend equipment
same practices

## Slide 12: Different Standards, Different PON Technologies
Point to Multi-Point FTTX Technologies
ITU-T G
IEEE 802.3
SCTE
BPON
622/155 Mbps
GPON
2.5/1.25 Gbps
XGPON-1
10/1.25 Gbps
XGS-PON
10/10 Gbps
NGPON2
40 Gbps
EPON
1/1 Gbps
10G EPON
10/1 Gbps
10/10 Gbps
NG-EPON
25/50/100 Gbps
RFoG
(DOCSIS Speeds)
CableLabs®
DPoE™
Notes: Traditional networks use active components to guide traffic. Devices such as processors, repeaters, and relays all require power to transmit data.
In contrast, passive optical networks use passive components that guide traffic based on splitting optical wavelengths to end points along the way. These passive components, such as splitters and coupler devices, work by passing or restricting light and do not require power to transmit data. Therefore, PONs use less power and cost less to operate.

## Slide 13: ITU Standards
The International Telecommunications Union (ITU) is an agency of the United Nations that is focused on telecommunications technologies. It was originally formed in 1865 as a way to standardize telegraph communications. The ITU eventually grew to also include wireless, satellite, maritime , & broadband technologies. www.itu.int
Examples of PON standards/technologies:
G.983 Broadband-capable PON (BPON)
G.984 Gigabit-capable PON (GPON)
G.987 10 Gigabit-capable PON (XG-PON1)
G.9807.1 10 Gigabit-capable Symmetrical PON (XGS-PON)
G.989 40 Gigabit-capable PON (NG-PON2)

## Slide 14: IEEE Standards
The Institute of Electrical and Electronics Engineers (IEEE) is a professional association created in 1963. Among other areas of electronic & electrical engineering, the IEEE also focuses on the development of telecommunications standards. www.ieee.org
Examples of PON Standards:
802.3ah Ethernet in the First Mile (EFM) 1G EPON
802.3av 10Gigabit EPON
802.3ca 25/50/100Gigabit EPON task force

## Slide 15: SCTE Standards
The Society of Cable and Telecommunications Engineers (SCTE) is a professional association focused on education and development of technologies related to cable telecommunications industry. www.scte.org
Examples of PON Standards:
RFoG SCTE 174-2010

## Slide 16: Cable Labs® Standards
Cable Labs® is a not-for-profit innovation and research and development lab founded in 1988 by American cable operators. System operators from around the world are eligible to be members. Cable Labs® was formed by the cable industry to build the foundational technology that now connects the modern world through research, development and innovation.
www.cablelabs.com
Examples of PON Standards:
DPoE™

## Slide 17: PON DS/US Wavelengths
*
*The original 1310nm optics were +/- 50 nm. Newer, narrower 1310nm optics are now generally available

## Slide 18: PON Parameters
Optical budget
Depends on class of optics
  Class A – 20dB
  Class B – 25dB GPON / PR20 EPON 24 dB
  Class B+ - 28dB GPON / PR30 EPON 29 dB
  Class C – 30dB GPON / PR40 EPON 33 dB
Most vendors have implemented Class B+ / PR30
Logical Reach
~20 Kilometers with 32 splits
Maximum distance between OLT and ONU
Split Ratio
1:128 estimated 4-6km
1:64 estimated 15-18 km
1:32 estimated 20-25 km
Depends on implementation
Typical Downstream (1490nm) Budget
OLT Launch Power = +3dBm
ONU Receive Sensitivity = 0dBm to -25dBm
Link Budget = 28dB
Typical Upstream (1310nm) Budget
ONU Launch Power = +1dBm
OLT Receive Sensitivity = -8dBm to -29dBm
Link Budget = 30dB*
Typical Downstream (1577nm) Budget
OLT Launch Power = +2dBm
ONU Receive Sensitivity = 0dBm to -28dBm
Link Budget = 30dB
Typical Upstream (1270nm) Budget
ONU Launch Power = +4dBm
OLT Receive Sensitivity = -8dBm to -28dBm
Link Budget = 32dB*
*Loss in fiber is higher at 1270/1310nm as compared to 1490/1577nm

## Slide 19: The Optical Splitter
Planar Splitter

## Slide 20: Network Losses
Fiber Loss + Splice/Connector Loss + Splitter Loss ≤ 28dB

## Slide 21: Typical Assumptions
Fiber Loss
Connector Loss
Splice Loss
Splitter Loss
@ 1310nm: 0.34dB/km or 0.00010363 dB/ft
@ 1490nm: 0.25db/km or 0.00007622 dB/ft
SC/APC: 0.25dB
0.05dB
1 x 2: 3.5dB
1 x 4 7.5dB
1 x 8 10.7dB
1 x 16 13.8dB
1 x 32 17.5dB
1 x 64 21.5dB

## Slide 22: Centralized Split
Loss Type | Connector | Splice | Fiber | Splitter | 
Loss | 4 @ .25dB Each | 10 @ 0.05dB Each | 20km @ 0.34/km | 1 x 32 | 
Total | 1.0dB | 0.5dB | 6.8dB | 17.5dB | 25.8dB
PON
Distribution
Fibers
ONT 1
Thru
ONT 32
ONT 1
ONT 32
Feeder
Fiber (19 km)
Drop Fiber (1km)
1 x 32
Splitter
-
17.5 dB
Loss
PON OLT

## Slide 23: Cascaded Splitters
Loss Type | Connector | Splice | Fiber | Splitter | 
Loss | 6 @ .25dB Each | 12 @ 0.05dB Each | 20km @ 0.34/km | 1x2, 1x4, 1x4 | 
Total | 1.5dB | 0.60dB | 6.8dB | 3.5dB+7.5dB+7.5dB | 27.4dB
ONT 1
1 x 2
splitter
ONT 2
ONT 3
ONT 4
ONT 11
ONT 12
ONT 14
ONT 5
ONT 6
ONT 8
ONT 9
ONT 10
ONT 13
ONT 7
Drop Fiber
Drop Fiber
Drop Fiber
1 x 4
Splitter
1 x 4
Splitter
1 x 4
Splitter
1 x 4
Splitter
Feeder
Fiber
4
3
-
-
3.5 dB
7.5 dB
7.5 dB
PON OLT

## Slide 24
PON Architectures

## Slide 25: Integrated PON (I-PON)
Challenge | Practical Considerations
Distance | Worst case (20 to 30 (km), less with larger split ratio)
Subscriber Density & Capacity | Worst case (32 ONUs per port, less at larger distances)
Trunk Fiber Conservation | Worst case
Headend / HUB Space & Power | Worst case
Management & Networking | Best case (uniform, centralized)

## Slide 26: I-PON + Repeater
Challenge | Practical Considerations
Distance | Middle case (Long reach DBA penalties are troublesome)
Subscriber Density & Capacity | Best case (128 ONUs per port)
Trunk Fiber Conservation | Best case
Headend / HUB Space & Power | Worst case
Management & Networking | Middle case (better if repeater is manageable)

## Slide 27: Remote PON (R-PON)
Challenge | Practical Considerations
Distance | Best case
Subscriber Density & Capacity | Best case (128 ONUs per port)
Trunk Fiber Conservation | Best case
Headend / HUB Space & Power | Middle case (additional Ethernet aggregation ports required)
Management & Networking | Worst case (many R-OLTs to network and manage)

## Slide 28: SDN PON (S-PON)
Challenge | Practical Considerations
Distance | Best case
Subscriber Density & Capacity | Best case (128 ONUs per port)
Trunk Fiber Conservation | Best case
Headend / HUB Space & Power | Best case (assuming shared spine/leaf switches)
Management & Networking | Unclear (can be best case if done well or worst case if not) At Comcast, this is more than the vDPoE Controller, it’s how they plan to do everything. Our solution MUST make it as simple and valuable as possible.

## Slide 29
RFoG: Radio Frequency over glass

## Slide 30: RFoG Network Benefits & Considerations
Fiber is run all the way to the premise thus creating a “future proof” outside plant.
Improved signal quality allows better utilization and higher data rates.
Ingress and RF issues are largely isolated to customer premise.
Technical expertise of headend & premise installations and technology is leveraged (no re-training).
Optical Beat Interference may impact upstream signals in an RFoG deployment.
Drops
Trunk
DOCSIS CMTS
VIDEO
Transmitter
Receiver
Fiber
RFoG
“Micro Node”
Notes: Highlight:
1 RPR vs. many
1 fiber vs. many
same headend equipment
same practices

## Slide 31: DOCSIS RFoG Network
Fiber
Coax
CM
RFoG Micro Node
Optical Splitter
1 x 32
20 km
λ = 1550 nm
λ = 1610 nm
DOCSIS CMTS
VIDEO
STB
MTA
Notes: Highlight:
1 RPR vs. many
1 fiber vs. many
same headend equipment
same practices

## Slide 32
RFoG
Fiber
Inside Coax Wiring
Ethernet, USB,
or wireless
Regular telephone wiring
MicroNode Coax Brick Powering Not Shown
Customer Premise Equipment (CPE) with MicroNodes
Single fiber supports both forward and return path
MicroNode provides optical to electrical conversion
5-42 / 54-1002MHz support
SC/APC connector towards fiber network
“F” connector to 75 ohm coax cable towards premise
Dedicated or inserted powering options
Spare ports available for other devices
RFoG Home Architecture & CPE

## Slide 33
OBI: Optical Beat Interference
Upstream interference caused when:
Two or more RFoG micro nodes transmit simultaneously
At very close or same wavelengths
Why would micro nodes transmit simultaneously?
STB transmitting while CM transmitting.
CM transmitting on one upstream while another CM transmitting on another US.

## Slide 34: OBI Example
DOCSIS CMTS
VIDEO
Fiber
Coax
CM 1
Coax
CM 2
RFoG Micro Node 1
Optical Splitter
1 x 32
λ = 1610 nm
t0: f=f1
t0: f=f2
RFoG Micro Node 2
t1: λ = 1610 nm
t2: OBI
Notes: Highlight:
1 RPR vs. many
1 fiber vs. many
same headend equipment
same practices

## Slide 35: Optical Beat Interference
Impacts of OBI include:
Return signal noise floor elevation
Service degradation on impacted CMTS receiver
Code word errors on CMTS upstream
Statistically chances of OBI will increase when:
Multiple upstreams are used (DOCSIS 3.0)
Number of active customers increase
Increase of upstream data being transmitted
DOCSIS CMTS
VIDEO
Fiber
Coax
CM 1
Coax
CM 2
RFoG Micro Node 1
Optical Splitter
1 x 32
λ = 1610 nm
t0: f=f1
t0: f=f2
RFoG Micro Node 2
t1: λ = 1610 nm
t2: OBI

## Slide 36: Addressing OBI – Active Splitter
Active splitters have been developed to prevent OBI by isolating the optical domain for each subscriber:
PROs:
By isolating optical domain, this can eliminate OBI.
Subtending splitters can scale to support over 1000 ONUs
Does not require site visit to change CPE for existing RFoG networks
CONs:
Requires powered facilities in the field
Requires 19” rack space in the field
First subscriber costs are extremely high for new deployments or less-dense applications
Active devices create additional points of failure in the network
May not be compatible with existing passive splitter deployments
DOCSIS CMTS
VIDEO
ACTIVE SPLITTER

## Slide 37: Addressing OBI – Selectable Upstream
R-ONUs are available with upstream wavelength conditioning that eliminate OBI:
PROs:
OBI is eliminated by not allowing R-ONUs to share the same wavelength.
Lower initial cost compared to active splitter solutions
Utilizes existing passive infrastructure
CONs:
Available wavelength selections are currently limited thus limiting the number of R-ONUs per splitter (currently 16)
Requires manual setting for each R-ONU to be effective
Requires detailed record keeping for all customer settings
Misconfiguration compromises OBI prevention
DOCSIS CMTS
VIDEO
Fiber
Optical Splitter
1 x 32
Coax
CM 1
Coax
CM 2
Coax
CM 3

## Slide 38: Addressing OBI – Wavelength Randomization
CONs:
Although mitigated extensively, OBI is not entirely eliminated
MicroNodes implement wavelength randomization to combat OBI:
PROs:
OBI is mitigated by randomly adjusting upstream wavelengths.
Lower initial cost compared to active splitter solutions
Utilizes existing passive infrastructure
No extensive record keeping
No manual configurations required
DOCSIS CMTS
VIDEO
Fiber
Optical Splitter
1 x 32
Coax
CM 1
Coax
CM 2
Coax
CM 3

## Slide 39
  Upstream
λ: 1610 nm
Tx: 3 dBm
Standard Micro Nodes
  Downstream
λ: 1550 nm
Rx: -6 to 0 dBm
CM
  Downstream
Freq.: 54 to 1002 MHz
Tx: 17 dBmV
  Upstream
Freq.: 5 to 42 MHz

## Slide 40
Micro Nodes: with a PON bypass filter
Downstream λ
RFoG: 1550 nm
1G EPON: 1490 nm
10G EPON: 1577nm
Upstream λ
RFoG: 1610 nm
1G EPON: 1310 nm
10G EPON: 1270nm
STB
10G
EPON
TV
PON Pass-Through

## Slide 41
OBI Mitigation Micro Nodes MND-1602-O
OBI Mitigating
Mitigates OBI by:
Using narrow spectrum laser to reduce interference probability; narrower than standard R-ONU
Randomizing wavelength via autonomous dynamic wavelength assignment (Lambda Motion™ Wavelength Randomization)

## Slide 42
Ethernet
Passive optical networking

## Slide 43: What is EPON?
Ideal for high bandwidth commercial and residential installations
MAC Layer Supports a 100 km service area, typical optical budgets support a 20 km service area with 1:32 split ratio.
10/1 Gbps Down x 10/1 Gbps Up symmetrical service to each PON
Gigabit Ethernet PON or Ethernet PON (GePON/EPON) is a Passive Optical Network access technology defined by IEEE 802.3ah and IEE 802.3av.
Uses separate wavelengths:
1G 1490 nm downstream & 1310 nm upstream.
10G 1577 nm downstream & 1270 nm upstream*
Notes: A PON is a passive optical network. There are no optical repeaters or other active devices in a PON, hence the name "passive." PONs are designed for local loop transmission rather than long distance and serve to bring fiber closer to the customer in order to obtain higher speed.
Since PONs are passive, they require less maintenance and provide higher reliability. Splitters are used to share network resources and are unpowered and unmanaged. Fiber provides extremely high bandwidth capabilities to carry voice, video, and data.

## Slide 44: EPON Components
IP Core
OLT
Voice
Switch
Internet
IPTV
Headend
OLT
ONUs
ONUs
Splitter
Splitter
PON
PON
Uplink
Uplink
EPON OLT - – An Optical Line Terminal aggregates all subscriber devices in a EPON network.
Passive Splitter – The passive splitter splits/combines numerous subscriber fiber drops into a single fiber run to the OLT. Although splits of up to 1:128 may be achieved, typical EPON deployments use up to a 32-way split serving 32 residences from a single OLT EPON port.
ONU- An EPON ONU is installed either outside or inside the subscribers premise and typically interfaces directly to the inside/premise wiring (coax, Ethernet, telephony).
Configuration of the ONU may occur through the OLT by means of Ethernet Operations Administration & Management (OAM) messages. Once online, the ONU may also receive configuration instructs to its IP address by a provisioning server.
Notes: OLT
An EPON system consists of an aggregation device called an optical line terminal (OLT). OLTs can be high dense chassis located in headend or hub locations, temperature hardened chassis in cabinet deployments, or node based solutions located within the outside plant. The OLT connects to the Outside Plant (OSP), or Optical Distribution Network (ODN), through PON interfaces. Connections to the service provider IP network core is accomplished through 1Gbps up to 100Gbps uplink interfaces.
Splitters
Splitters passively divide optical energy from an input port into any number of output ports. Although splits of up to 1:128 may be achieved, typical EPON deployments use up to a 32-way split serving 32 residences from a single OLT EPON port. These splitters can be located anywhere, at the serving office or closer to the served area, reducing fiber costs. Individual fibers run from each residence back to the splitter.
ONU
In an EPON network, subscriber’s voice, video, and data devices are connected to the PON via the ONU.
The ONU associates IP Voice/Video/Data traffic by Logical Link Identifier (LLID) and combines/splits the signal with analog and/or digital video to and from the OLT.
An EPON ONU is installed either outside or inside the subscribers premise and typically interfaces directly to the inside/premise wiring (coax, Ethernet, telephony).
Configuration of the ONU may occur through the OLT by means of Ethernet Operations Administration & Management (OAM) messages. Once online, the ONU may also receive configuration instructs to its IP address by a provisioning server.

## Slide 45: 10G-EPON Network Details
DS: 1577nm
US: 1270nm
Up to 20km*
Receiver Sensitivity
OLT: Approximately -28dBm
ONU: Approximately -28.5dBm
These values vary based on optics. Check vendor documentation for details
Transmit Power
Measured launch power at OLT +2 to +5dBm
Due to a burst mode transmitter, power level at the ONT may be difficult to measure and requires an inline power meter. Launch power at ONT may be up to +9dBm
10Gig EPON Optics |  |  |  | 
Optics | PR10 | PR20 | PR30 | PR40
Max. Loss | 20dB | 24dB | 29dB | 33dB
1/10Gig Co-existence EPON Optics |  |  |  | 
Optics | PRX10 | PRX20 | PRX30 | PRX40
Max. Loss | 20dB | 24dB | 29dB | 33dB

## Slide 46
Downstream
Notes: The OLT learns the ONU MAC address in the discovery process which triggers the creation of a “virtual cable modem”, or “vCM”. The vCM requests an IP address from the DHCP server and is told what configuation file to download and where the tftp server is located. When the configuration file is received the vCM translates the DOCSIS TLVs into DPoE OAM which is sent to the ONU for provisioning. Upon completion of processing the OAM messages, provisioning is completed and IP connectivitiy to the subscriber is established. MTAs for VoIP, RGs for data, or other services at the subscriber premise or embedded in the subscriber equipment can then use the IP connectivity to complete there service provisioning depending on the customer’s acquired services.
The OLT forwards all traffic downstream towards the PON. This would imply that each ONU is subjected to all traffic destined to the entire PON. In order to minimize the amount of traffic processing, and not to mention security concerns, the OLT assigns one or more Logical Link IDentifiers (LLIDs) to an ONU. Early EPON implementations used an LLID per ONU to manage traffic with some vendors also implementing a “broadcast LLID” which was share amoungst multiple ONUs. With newer implementations each ONU can host numerous LLIDs in an effort to better segregate and manage certain traffic types. For example, today an ONU may have an LLID for best effort data, one for VoIP, one for WiFi, and one for multicast traffic.

## Slide 47
Upstream
Notes: Immediately after powering up the ONU will look for a downstream signal. If one is available it will listen for a discovery window that will inform the ONU when it is ok to advertise that it is on the PON. Once the discovery window is known the ONU will advertise itself by means of its MAC address. The OLT will validate whether the ONU is permitted on the PON through its admission control and, if allowed, will proceed with further provisioning processes (either EMS, CLI, or DPoE).

## Slide 48: EPON Upstream Co-Existence

## Slide 49: Co-existence Options

## Slide 50: 10G-EPON Summary
Defined by IEEE 802.3av-2009 10G-EPON
EPON is a point-to-multipoint, Passive Optical Network technology
Optical wavelengths used are 1577nm in the downstream & 1270nm in the upstream
Can coexist with existing IEEE 802.3ah EPON solutions
Native end-to-end Ethernet solution
Supports voice, data, and video (RF overlay or IPTV)
Symmetrical bandwidth per port. (Downstream rate 10Gbps, Upstream rate 10Gbps)
Bandwidth is shared across subscribers on each PON port.
Each PON port typically supports 32 subscribers and a service area of 20km
Can use a proprietary management platform or existing DOCSIS provisioning system

## Slide 51
EPON Evolution
EPON Standard Evolution:
  802.3ah: 1G/1G specification (2004)
  802.3av: 10G/10G specification (2009)
  DPoE v1: DOCSIS Provisioning over EPON (2011)
  DPoE v2: DOCSIS Provisioning over EPON (2012)
  SIEPON: Service Interoperability in Ethernet Passive Networks (2013)
  NG-EPON: IEEE already working on next generation 802.3 EPON for 25/50/100Gbps speeds
2004 802.3ah
2009 802.3av
2011 DPoEv1
2012 DPoEv2
2013 SIEPON
(2019?) NG-EPON

## Slide 52
EPON as Universal Fiber Access Architecture

## Slide 53
Docsis Provisioning of EPON (DPoE)

## Slide 54: What is DOCSIS Provisioning of EPON
DOCSIS
EPON
DPoE

## Slide 55: DPoE Specifications
CableLabs qualified the first DPoE v1.0 hardware systems in June 2013. The process of qualifying meant that submitted equipment must adhere to the specifications list in the following areas:
DPoE Architecture Specification (ARCH)
DPoE IP Network Element Specification (IPNE)
DPoE Metro Ethernet Forum Specification (MEF)
DPoE MAC & Upper Layer Protocols (MULPI)
DPoE OAM Extensions Specification (OAM)
DPoE Operations Support System Interface specification (OSSI)
DPoE Physical Layer Specification (PHY)
DPoE Security & Certificate Specification (SEC)

## Slide 56
There are millions of DOCSIS cable modems (CMs) that continued to be deployed and managed worldwide
Cable Operators want to leverage their investment and expertise by using the same Operations and Support Systems (OSS) with any access technologies.
CableLabs certification process
Multi-vendor interoperability between OLTs & ONUs
Multigigabit high speed data services
Metro Ethernet commercial service capabilities
Benefits of DPoE
Notes: DPoE makes use of the well established DOCSIS provisioning tools deployed by worldwide Cable operators. This allows service providers to deploy services across an all fiber EPON network in much the same manner as their exisiting DOCSIS network. Not only are there significant cost savings in the re-use of the existing OSS/BSS integration but there are substantial operational benefits since technical staff will not have to adapt to this new technology and may leverage much of their existing experience in the new access architecture.

## Slide 57: Comparison of DOCSIS and DPoE Network DOCSIS 3.1 HFC Network
DOCSIS Back Office OSS
HFC Network
Customer Premise
DHCPv4
Server
DHCPv6
Server
SNMP
Manager
Syslog
Server
Time
Server
TFTP
Server
CMTS
Cable
Modem
Cable
Modem
IPv4
CPE
IPv6
CPE
IPv4
CPE
IPv6
CPE

## Slide 58: Comparison of DOCSIS and DPoE Network With DPoE Emulation Engine
OLT
DHCPv4
Server
DHCPv6
Server
SNMP
Manager
Syslog
Server
Time
Server
TFTP
Server
ONU
ONU
IPv4
CPE
IPv6
CPE
IPv4
CPE
IPv6
CPE
DOCSIS Back Office OSS
PON Network
Customer Premise
vCM
DML
L3

## Slide 59: DPoE - DPoE Emulation Engine
The DPoE Emulation Engine is the entity or process on the DPoE system that translates all DOCSIS specific management tools into EPON, some of its tasks are:
Interprets the DOCSIS MIBs
Creates virtual Cable Modems (vCMs) for every ONU and requests IP addresses and configuration files for them.
Translates the parameters received in the configuration file for each vCM to EPON OAM messages for the ONU.
Keeping ONU software load up to date using the DOCSIS secure software download mechanism with digitally signed software images
Provides a CLI that “looks and feels” like a CMTS
Notes: DPoE combines DOCSIS Provisioning (DHCP, TFTP, binary cfg files, SNMP, etc) with an EPON access platform. In order to be successful there must exist an entity that provides translations between traditional DOCSIS management and EPON management. This translation is commonly refered to as the DOCSIS Mediation Layer or “DML”. The DML may be embedded in the OLT itself or exist on an outside server to manage one or more OLTs. The sole purpose of DML is to enable the successful provisioning of subscriber services as if the system were a traditional CMTS & cable modem network. This is largely accomplished by representing each ONU as a virtual cable modem, “vCM”.

## Slide 60: DPoE – OLT Functionality (Layer-3)
The OLT serves as a layer 3 device which aggregates subscriber equipment and services much the same way the CMTS does.
Similar to the CMTS the OLT will support numerous routing protocols and features.
Many CLI commands and interface references also mirror that of a CMTS.
Most customer configurations found on a CMTS can be used as a reference for initial OLT configuration and setup.
Additionally the OLT supports the Virtual Cable Modem and DOCSIS Mediation Layer functionalities.
The OLT as a CMTS with PON ports…

## Slide 61: DPoE – Virtual Cable Modem (vCM)
The vCM is a software entity that exists in the OLT, or on the server hosting the DPoE software and not on the ONU itself.
The purpose of the vCM is to present itself as a cable modem to the DOCSIS provisioning system, obtain an IP address, request a configuration file, and interpret the DOCSIS TLVs into DPoE OAM that the ONU understands for provisioning itself.
In addition the vCM will serve as a managed entity for any SNMP queries used to extract data from the ONU.
In many ways the vCM can be viewed as a proxy for the ONU.

## Slide 62: DPoE– ONU initialization
MAC - 0024.0001.0002
MAC Address
0024.0001.0002
When ONUs first come online they look for a valid downstream signal from the OLT. For 10G EPON (IEEE-802.3av) the downstream optical wavelength will be at 1577nm.
Once the wavelength is confirmed and a discovery window is recognized, the ONU will advertise itself by means of its MAC address.
For 10G EPON (IEEE-802.3av) the upstream optical wavelength will be at 1270nm.

## Slide 63: DPoE– vCM Initialization
vCM - 0024.0001.0002
MAC Address
0024.0001.0002
The OLT learns the ONU MAC address in the discovery process which triggers the creation of a “virtual cable modem”, or “vCM” in the DML software.

## Slide 64: DML – DHCP and TFTP
vCM - 0024.0001.0002
The vCM requests an IP address from the DHCP server and is told what configuration file to download and where the tftp server is located.
DHCP
TFTP

## Slide 65: DML – Service Instantiation
When the configuration file is received the vCM translates the DOCSIS TLVs into DPoE OAM which is sent to the ONU for provisioning. Upon completion of processing the OAM messages, provisioning is completed and IP connectivity to the subscriber is established.
vCM - 0024.0001.0002
TFTP
MAC - 0024.0001.0002
MAC Address
0024.0001.0002
DOCSIS TLVs
DPoE OAM

## Slide 66
GPON
Gigabit Passive Optical Networking

## Slide 67: What is GPON?
Ideal for high bandwidth commercial and residential installations
MAC Layer Supports a 60 km service area, typical optical budgets support a 20 km service area with 1:32 split ratio.
Gigabit PON is a Passive Optical Network access technology defined by ITU-T G.984 Gigabit-capable PON (GPON) that runs at 2.5/1.25 Gbps speeds. There is also 10/10 Gbps XGS-PON (G.9807.1) and 40 Gbps NGPON2 (G.989)
GPON Uses separate wavelengths:
1G 1490 nm downstream & 1310 nm upstream.
10G (XGS-PON) 1577 nm downstream & 1270 nm upstream
Notes: A PON is a passive optical network. There are no optical repeaters or other active devices in a PON, hence the name "passive." PONs are designed for local loop transmission rather than long distance and serve to bring fiber closer to the customer in order to obtain higher speed.
Since PONs are passive, they require less maintenance and provide higher reliability. Splitters are used to share network resources and are unpowered and unmanaged. Fiber provides extremely high bandwidth capabilities to carry voice, video, and data.

## Slide 68: GPON Reference Architecture
Phone
HDTV
Set-Top
Box
Phone
Internet
Total Access 5000
Central Office
Internet
IPTV Head END
Voice Switch
IP Core
Splitter
ONT
Internet
ONT
Optical Line Terminal (OLT): at the TA5K
Optical Distribution Network (ODN): Fiber / Splitter
Optical Network Terminal (ONT): at the customer premises
OLT
Notes: A PON consists of a central office node, called an optical line terminal (OLT), one or more user nodes, called optical network units (ONUs) or optical network terminals (ONTs), and the fibers and splitters between them, called the optical distribution network (ODN). ONT is an ITU-T term, whereas ONU is an IEEE term.
The splitter can be up to a 32-way split serving 32 residences from a single OLT GPON port. This splitter can be located anywhere, at the serving office or closer to the served area, reducing fiber costs. Individual fibers run from each residence back to the splitter.
In this type of network, subscriber’s voice, video, and data devices are connected to the GPON via the ONT.
The ONT formats IP data and analog voice into GPON Encapsulated Mode (GEM) frames and combines/splits the signal with analog and/or digital video to and from the OLT.

## Slide 69: OMCI - ONT Management Control Interface
ONT Management and Control Interface
A GEM connection is established by the OLT when the ONT comes online, then OMCI runs across that connection
Establishes and release connections across the ONT
Manages the UNIs at the ONT
Request configuration information and performance statistics
Informs the system of events such as link failures
OLT manages the ONT
Defined by ITU specification G.984.4.
Provides for the encryption method, known as churning, that allows only the proper destination ONT to decrypt frames sent to it by the OLT.

## Slide 70: GPON Overview Downstream GEM
GEM Port: A GPON Encapsulation Method (GEM) port is a virtual port for performing encapsulation for transmitting Ethernet frames or ATM cells between the OLT and the ONU/ONT. GEM is based on the ITU-T G.7041 Generic Framing Procedure.
Each different traffic-class (TC) per UNI is assigned a different GEM Port
an example could be:
GEM 0x101 = Voice (PBIT 5) for ONT #1
GEM 0x102 = Internet (PBIT 0,1,2) for ONT #1
GEM 0x103 = Video (PBIT 3,4) for ONT #1
Each GEM port is assigned a GEM-Port ID (0 to 4095) by the OLT. A GEM-Port ID can only be used once per OLT port. On the ADTRAN TA5000, downstream GEM-Port ID #1023 is reserved for Multicast traffic to ALL ONTs (IPTV).
ONT
GEM1
GEM2
GEM3
GPON
Interface
OLT
GEM1
GEM2
GEM3
GPON
Interface
DOWNSTREAM
VOICE
INET
VIDEO
VOICE
INET
VIDEO
UNI

## Slide 71: GPON Overview Upstream GEM
ONT
In the upstream direction, GEM(s) are assigned into T-CONTs (traffic containers). Each TCONT is given a GRANT by the OLT as a “allowed time to transmit”. This GRANT is what gives each customer a specific (or varied by DBA) upstream speed.
GEM1
GEM2
GEM3
TCONT
1
TCONT2
GPON
Interface
OLT
GEM1
GEM2
GEM3
TCONT
1
TCONT2
GPON
Interface
GPON UPSTREAM
TCONT1 GRANT
TCONT2 GRANT

## Slide 72: GPON Overview - Downstream
OLT
ONT #1
ONU-ID
0
DOWNSTREAM
ONT #2
ONU-ID
1
ONT #3
ONU-ID
2
1xN
DOWNSTREAM
DOWNSTREAM
DOWNSTREAM
All Downstream traffic is “seen” by all ONTs. This is a potential security concern for Unicast traffic.
Pin #: 1234
Pin #: 1234
Pin #: 1234

## Slide 73: GPON Overview - AES
AES Encryption is used to secure UNICAST traffic.
Only the ONT with the correct decryption key can decode the packet.
Encryption keys are exchanged during ONT Activation and every 30 minutes thereafter.
OLT
ONT #1
ONU-ID
0
DOWNSTREAM
ONT #2
ONU-ID
1
ONT #3
ONU-ID
2
1xN
DOWNSTREAM
DOWNSTREAM
DOWNSTREAM
HI MOM@ONT#1
KEY0
KEY0
KEY0
KEY0
KEY1
KEY2

## Slide 74: GPON Overview - Upstream Grants
OLT
ONT #1
ONU-ID
0
ONT #2
ONU-ID
1
ONT #3
ONU-ID
2
We use a dynamic form of TDMA (Time-Division Multiple Access), where each ONT is periodically allocated a time-slot to transmit in. This process is called a “GRANT”
The OLT is always in charge and will change grant timing based on several variables.
A malfunctioning ONT can go “Rogue” by transmitting outside of its grant.
UPSTREAM
UPSTREAM
UPSTREAM
UPSTREAM
1xN

## Slide 75: GPON Overview Upstream DBA
What happens when more bandwidth is allocated than is actually available on the PON? For example, when 3x 1G upstream customers are on the same PON and all need to send 1Gb of traffic upstream?
OLT
1xN
UPSTREAM
UPSTREAM
UPSTREAM
UPSTREAM
ONT #1
ONU-ID
0
ONT #2
ONU-ID
1
ONT #3
ONU-ID
2
1Gb
DBA – Dynamic Bandwidth Allocation
steps in and the OLT GRANTs a “fair” amount of bandwidth to each ONT until their queues are empty.
1Gb
1Gb

## Slide 76: The Future of PON (NG-PON2)
10Gbps symmetric
Optical budget similar to GPON B+
Nominal 32 splits at 20km
Can coexist with GPON on same ODN
Supports multiple 10G PONs on same ODN at different wavelength pairs
Easy capacity expansion
Fixed or tunable (colorless) optics
Standard allows a single ONT to tune across 4 wavelengths
Supports adding point-to-point wavelengths
Dedicated bandwidth, optical P2P on physical PON ODN
10Gbps downstream, 2.5 Gbps upstream also possible.
Makes rollouts and migration easier
Multiple services can be multiplexed onto the same ODN. This keeps outside plant costs to a minimum
Each group gets their own wavelength with, instead of a 20nm band like upstream GPON, one band at less than 1nm spacing.
NGPON2
+
4-8 TDM
PON λs
WDM
Overlay λs
=
The future of PON relies on WDM-PON solutions like NG-PON2 (defined by ITU-T G.989). We can provide customers with their own wavelength, which could allow >10Gbps symmetrical data transfer.
The tunable optics are expensive. How do we provide 10G service before prices come down?

## Slide 77: The Future of PON (XGS-PON)
10Gbps symmetric
Optical budget similar to GPON B+
Nominal 32 ONTs at 20km
Can coexist with GPON on same ODN
Allows 10G service without major network changes
Can use 10G EPON wavelengths (1577nm downstream, 1270nm upstream)
Can also use traditional GPON wavelengths for greenfield installations
Only changes are OLT and ONT hardware
Provisioning nearly identical to GPON process
Same bandwidth per PON as NG-PON2
Support for up to 64 ONTs
What about a bridge between the changes for NG-PON2 and current GPON?
XGS-PON bridges the gap.
GPON
XGS-PON
CWDM
splitter
GPON ONT
XGS-PON ONT
GPON and XGS-PON co-existence with CWDM
1490/1310
1577/1270

## Slide 78
Questions?